## Slide 1: Computer Architecture
Lab 7

## Slide 2
  MIPS Instruction Set Architecture

## Slide 3: Memory in MIPS
100 | 8 bits
101 | 8 bits
102 | 8 bits
103 | 8 bits
104 | 8 bits
105 | 8 bits
Memory
Instruction / Data
To store any value in the memory you need 4 cells

## Slide 4: Save Value in the Memory
Num1: .word 5
Memory
100 | 5
101 | 8 bits
102 | 8 bits
103 | 8 bits
104 | 
105 | 
106 | 
107 | 
The starting address of the memory cells where the data will be saved which is 100
Num1

## Slide 5: Read Value from the Memory
la $s0, Num1
Memory
100 | 5
101 | 8 bits
102 | 8 bits
103 | 8 bits
104 | 
105 | 
106 | 
107 | 
Num1
lw $s1, 0($s0)
Load the address Num1 and save it in register s0
Load the data from the address in s0 + 3 more cells and save it in register s1
Contains Address 100
Contains
Data=5
Contains
Address=100

## Slide 6: Store Value back in the Memory
sw $s4, 0($s1)
Memory
100 | 5
101 | 8 bits
102 | 8 bits
103 | 8 bits
104 | 0
105 | 
106 | 
107 | 
Num1
la $s1, Num2
Num2: .word 0
li $S4, 6
Num2
Contains the starting Address where the data will be saved

## Slide 7
.globl main
.data
Num1: .word 5
Num2: .word 3
Num3: .word 2
RES: .word 0
.text
main:
la $t1, Num1
la $t2, Num2
la $t3, Num3
la $t4, RES
lw $s1, 0($t1)
lw $s2, 0($t2)
lw $s3, 0($t3)
add $t5, $s1, $s2
add $s4, $t5, $s3
sw $s4, 0($t4)
li $v0,10
syscall

## Slide 8
.globl main
.data
Num1: .word 5
Num2: .word 3
Num3: .word 2
RES: .word 0
.text
main:
la $t1, Num1
lw $s1, 0($t1)
addi $t1,4
lw $s2, 0($t1)
addi $t1,4
lw $s3, 0($t1)
add $t5, $s1, $s2
add $s4, $t5, $s3
addi $t1,4
sw $s4, 0($t1)
li $v0,10
syscall

## Slide 9
Counter for the 8 elements
Read the data from the memory
Loop over the 8 elements
Increment the address
Increment the loop counter
Store the sum
Store the avg

## Slide 10
AB 5F
00 FF and
----------------------
00 5F
AB5F
AB00
005F
AB 5F
FF 00 and
----------------------
AB 00
5F00
00AB
Logical Shift Left
Logical Shift Right
5FAB
or